## Slide 1: Design of Digital Circuits Lecture 24a: Multiprocessor Caches
Prof. Onur Mutlu
ETH Zurich
Spring 2019
23 May 2019

## Slide 2: Readings
Caches
Required
  H&H Chapters 8.1-8.3
  Refresh: P&P Chapter 3.5
Recommended
  An early cache paper by Maurice Wilkes
    Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.

## Slide 3: Recall: Cache Structure
Address
Tag Store
(is the address
in the cache?
+ bookkeeping)
Data Store
(stores
memory
blocks)
Hit/miss?
Data

## Slide 4: Cache Performance

## Slide 5: Recall: Cache Parameters vs. Miss/Hit Rate
Cache size
Block size
Associativity
Replacement policy
Insertion/Placement policy

## Slide 6: Recall: How to Improve Cache Performance
Three fundamental goals
Reducing miss rate
  Caveat: reducing miss rate can reduce performance if more costly-to-refetch blocks are evicted
Reducing miss latency or miss cost
Reducing hit latency or hit cost
The above three together affect performance

## Slide 7: Recall: Improving Basic Cache Performance
Reducing miss rate
  More associativity
  Alternatives/enhancements to associativity
    Victim caches, hashing, pseudo-associativity, skewed associativity
  Better replacement/insertion policies
  Software approaches
Reducing miss latency/cost
  Multi-level caches
  Critical word first
  Subblocking/sectoring
  Better replacement/insertion policies
  Non-blocking caches (multiple cache misses in parallel)
  Multiple accesses per cycle
  Software approaches

## Slide 8: Recall: Software Approaches for Higher Hit Rate
Restructuring data access patterns
Restructuring data layout
Loop interchange
Data structure separation/merging
Blocking
…

## Slide 9: Recall: Restructuring Data Access Patterns (I)
Idea: Restructure data layout or data access patterns
Example: If column-major
  x[i+1,j] follows x[i,j] in memory
  x[i,j+1] is far away from x[i,j]
This is called loop interchange
Other optimizations can also increase hit rate
  Loop fusion, array merging, …
Poor code
for i = 1, rows
for j = 1, columns
sum = sum + x[i,j]
  Better code
  for j = 1, columns
  for i = 1, rows
  sum = sum + x[i,j]

## Slide 10: Recall: Restructuring Data Access Patterns (II)
Blocking
  Divide loops operating on arrays into computation chunks so that each chunk can hold its data in the cache
  Avoids cache conflicts between different chunks of computation
  Essentially: Divide the working set so that each piece fits in the cache
Also called Tiling

## Slide 11: Restructuring Data Layout (I)
Pointer based traversal (e.g., of a linked list)
Assume a huge linked list (1B nodes) and unique keys
Why does the code on the left have poor cache hit rate?
  “Other fields” occupy most of the cache line even though rarely accessed!
struct Node {
struct Node* next;
int key;
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access other fields of node
}
node = nodenext;
}

## Slide 12: Restructuring Data Layout (II)
Idea: separate frequently-used fields of a data structure and pack them into a separate data structure
Who should do this?
  Programmer
  Compiler
    Profiling vs. dynamic
  Hardware?
  Who can determine what is frequently used?
struct Node {
struct Node* next;
int key;
struct Node-data* node-data;
}
struct Node-data {
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access nodenode-data
}
node = nodenext;
}

## Slide 13: Multi-Core Issues in Caching

## Slide 14: Caches in a Multi-Core System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 15: Caches in Multi-Core Systems
Cache efficiency becomes even more important in a multi-core/multi-threaded system
  Memory bandwidth is at premium
  Cache space is a limited resource across cores/threads
How do we design the caches in a multi-core system?
Many decisions
  Shared vs. private caches
  How to maximize performance of the entire system?
  How to provide QoS to different threads in a shared cache?
  Should cache management algorithms be aware of threads?
  How should space be allocated to threads in a shared cache?

## Slide 16: Private vs. Shared Caches
Private cache: Cache belongs to one core (a shared block can be in multiple caches)
Shared cache: Cache is shared by multiple cores
CORE 0
CORE 1
CORE 2
CORE 3
L2
CACHE
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
L2
CACHE
CORE 0
CORE 1
CORE 2
CORE 3
DRAM MEMORY CONTROLLER
L2
CACHE

## Slide 17: Resource Sharing Concept and Advantages
Idea: Instead of dedicating a hardware resource to a hardware context, allow multiple contexts to use it
  Example resources: functional units, pipeline, caches, buses, memory
Why?
+ Resource sharing improves utilization/efficiency  throughput
  When a resource is left idle by one thread, another thread can use it; no need to replicate shared data
+ Reduces communication latency
  For example, data shared between multiple threads can be kept in the same cache in multithreaded processors
+ Compatible with the shared memory programming model

## Slide 18: Resource Sharing Disadvantages
Resource sharing results in contention for resources
  When the resource is not idle, another thread cannot use it
  If space is occupied by one thread, another thread needs to re-occupy it
- Sometimes reduces each or some thread’s performance
- Thread performance can be worse than when it is run alone
- Eliminates performance isolation  inconsistent performance across runs
- Thread performance depends on co-executing threads
- Uncontrolled (free-for-all) sharing degrades QoS
- Causes unfairness, starvation
Need to efficiently and fairly utilize shared resources

## Slide 19: Private vs. Shared Caches
Private cache: Cache belongs to one core (a shared block can be in multiple caches)
Shared cache: Cache is shared by multiple cores
CORE 0
CORE 1
CORE 2
CORE 3
L2
CACHE
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
L2
CACHE
CORE 0
CORE 1
CORE 2
CORE 3
DRAM MEMORY CONTROLLER
L2
CACHE

## Slide 20: Shared Caches Between Cores
Advantages:
  High effective capacity
  Dynamic partitioning of available cache space
    No fragmentation due to static partitioning
    If one core does not utilize some space, another core can
  Easier to maintain coherence (a cache block is in a single location)
Disadvantages
  Slower access (cache not tightly coupled with the core)
  Cores incur conflict misses due to other cores’ accesses
    Misses due to inter-core interference
    Some cores can destroy the hit rate of other cores
  Guaranteeing a minimum level of service (or fairness) to each core is harder (how much space, how much bandwidth?)

## Slide 21: Example: Problem with Shared Caches
L2 $
L1 $
……
Processor Core 1
L1 $
Processor Core 2
←t1
  Kim et al., “Fair Cache Sharing and Partitioning in a Chip Multiprocessor Architecture,” PACT 2004.

## Slide 22: Example: Problem with Shared Caches
L1 $
Processor Core 1
L1 $
Processor Core 2
L2 $
……
t2→
  Kim et al., “Fair Cache Sharing and Partitioning in a Chip Multiprocessor Architecture,” PACT 2004.

## Slide 23: Example: Problem with Shared Caches
L1 $
L2 $
……
Processor Core 1
Processor Core 2
←t1
L1 $
t2→
t2’s throughput is significantly reduced due to unfair cache sharing.
  Kim et al., “Fair Cache Sharing and Partitioning in a Chip Multiprocessor Architecture,” PACT 2004.

## Slide 24: Memory System: A Shared Resource View
Storage
Most of the system is a shared resource, storing and moving data

## Slide 25: Cache Coherence

## Slide 26: Cache Coherence
Basic question: If multiple processors cache the same block, how do they ensure they all see a consistent state?
P1
P2
x
Interconnection Network
Main Memory
1000

## Slide 27: The Cache Coherence Problem
P1
P2
x
Interconnection Network
Main Memory
ld r2, x
1000
1000

## Slide 28: The Cache Coherence Problem
P1
P2
x
Interconnection Network
Main Memory
ld r2, x
ld r2, x
1000
1000
1000

## Slide 29: The Cache Coherence Problem
P1
P2
x
Interconnection Network
Main Memory
ld r2, x
add r1, r2, r4
st x, r1
ld r2, x
1000
1000
2000

## Slide 30: The Cache Coherence Problem
P1
P2
x
Interconnection Network
Main Memory
ld r2, x
add r1, r2, r4
st x, r1
ld r2, x
1000
1000
2000
ld r5, x
Should NOT load 1000

## Slide 31: Cache Coherence: Whose Responsibility?
Software
  Can the programmer ensure coherence if caches are invisible to software?
  What if the ISA provided a cache flush instruction?
    FLUSH-LOCAL A: Flushes/invalidates the cache block containing address A from a processor’s local cache.
    FLUSH-GLOBAL A: Flushes/invalidates the cache block containing address A from all other processors’ caches.
    FLUSH-CACHE X: Flushes/invalidates all blocks in cache X.
Hardware
  Simplifies software’s job
  One idea: Invalidate all other copies of block A when a processor writes to it

## Slide 32: A Very Simple Coherence Scheme (VI)
Caches “snoop” (observe) each other’s write/read operations. If a processor writes to a block, all others invalidate the block.
A simple protocol:
Write-through, no-write-allocate cache
Actions of the local processor on the cache block: PrRd, PrWr,
Actions that are broadcast on the bus for the block: BusRd, BusWr
PrWr / BusWr
Valid
BusWr
Invalid
PrWr / BusWr
PrRd / BusRd
PrRd/--

## Slide 33: (Non-)Solutions to Cache Coherence
No hardware based coherence
  Keeping caches coherent is software’s responsibility
  + Makes microarchitect’s life easier
  -- Makes average programmer’s life much harder
    need to worry about hardware caches to maintain program correctness?
  -- Overhead in ensuring coherence in software (e.g., page protection and page-based software coherence)
All caches are shared between all processors
  + No need for coherence
  -- Shared cache becomes the bandwidth bottleneck
  -- Very hard to design a scalable system with low-latency cache access this way

## Slide 34: Maintaining Coherence
Need to guarantee that all processors see a consistent value (i.e., consistent updates) for the same memory location
Writes to location A by P0 should be seen by P1 (eventually), and all writes to A should appear in some order
Coherence needs to provide:
  Write propagation: guarantee that updates will propagate
  Write serialization: provide a consistent order seen by all processors for the same memory location
Need a global point of serialization for this store ordering

## Slide 35: Hardware Cache Coherence
Basic idea:
  A processor/cache broadcasts its write/update to a memory location to all other processors
  Another cache that has the location either updates or invalidates its local copy
Two major approaches
  Snoopy bus
  Directory based
To learn more, take the Graduate Comp Arch class
  https://safari.ethz.ch/architecture/fall2018/doku.php?id=schedule

## Slide 36: Design of Digital Circuits Lecture 24a: Multiprocessor Caches
Prof. Onur Mutlu
ETH Zurich
Spring 2019
23 May 2019

## Slide 37: Cache Examples: For You to Study

## Slide 38: Cache Terminology
Capacity (C):
  the number of data bytes a cache stores
Block size (b):
  bytes of data brought into cache at once
Number of blocks (B = C/b):
  number of blocks in cache: B = C/b
Degree of associativity (N):
  number of blocks in a set
Number of sets (S = B/N):
  each memory address maps to exactly one cache set

## Slide 39: How is data found?
Cache organized into S sets
Each memory address maps to exactly one set
Caches categorized by number of blocks in a set:
  Direct mapped: 1 block per set
  N-way set associative: N blocks per set
  Fully associative: all cache blocks are in a single set
Examine each organization for a cache with:
  Capacity (C = 8 words)
  Block size (b = 1 word)
  So, number of blocks (B = 8)

## Slide 40: Direct Mapped Cache

## Slide 41: Direct Mapped Cache Hardware

## Slide 42: Direct Mapped Cache Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
42

## Slide 43: Direct Mapped Cache Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 3/15 = 20%
Temporal Locality Compulsory Misses
43

## Slide 44: Direct Mapped Cache: Conflict
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
44

## Slide 45: Direct Mapped Cache: Conflict
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 10/10 = 100%
Conflict Misses
45

## Slide 46: N-Way Set Associative Cache

## Slide 47: N-way Set Associative Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
47

## Slide 48: N-way Set Associative Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 2/10
= 20%
Associativity reduces conflict misses
48

## Slide 49: Fully Associative Cache
No conflict misses
Expensive to build
49

## Slide 50: Spatial Locality?
Increase block size:
  Block size, b = 4 words
  C = 8 words
  Direct mapped (1 block per set)
  Number of blocks, B = C/b = 8/4 = 2
50

## Slide 51: Direct Mapped Cache Performance
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
51

## Slide 52: Direct Mapped Cache Performance
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 1/15
= 6.67%
Larger blocks reduce compulsory misses through spatial locality
52

## Slide 53: Cache Organization Recap
Main Parameters
  Capacity: C
  Block size: b
  Number of blocks in cache: B = C/b
  Number of blocks in a set: N
  Number of Sets: S = B/N
Organization | Number of Ways (N) | Number of Sets (S = B/N)
Direct Mapped | 1 | B
N-Way Set Associative | 1 < N < B | B / N
Fully Associative | B | 1
53

## Slide 54: Capacity Misses
Cache is too small to hold all data of interest at one time
  If the cache is full and program tries to access data X that is not in cache, cache must evict data Y to make room for X
  Capacity miss occurs if program then tries to access Y again
  X will be placed in a particular set based on its address
In a direct mapped cache, there is only one place to put X
In an associative cache, there are multiple ways where X could go in the set.
How to choose Y to minimize chance of needing it again?
  Least recently used (LRU) replacement: the least recently used block in a set is evicted when the cache is full.

## Slide 55: Types of Misses
Compulsory: first time data is accessed
Capacity: cache too small to hold all data of interest
Conflict: data of interest maps to same location in cache
Miss penalty: time it takes to retrieve a block from lower level of hierarchy

## Slide 56: LRU Replacement
# MIPS assembly
lw $t0, 0x04($0)
lw $t1, 0x24($0)
lw $t2, 0x54($0)
56

## Slide 57: LRU Replacement
# MIPS assembly
lw $t0, 0x04($0)
lw $t1, 0x24($0)
lw $t2, 0x54($0)
57